DS6700 Specification Highlights

Physical Characteristics

Dimensions 6.55 in. H x 2.82 in. W x 4.72 in. D 16.64 cm H x 7.16 cm W x 11.99 cm D Weight (without cable) 6.04 oz./181.4 gm Input Voltage 5 volts +/- 10% Operating Current 250mA (average) Power Sources Depending on host: •Host power •External power supply Colors Cash Register White or Twilight Black

Performance Characteristics

Light Source 650 nm visible laser diode Resolution 640 x 480 Minimum Element Width 5 mil/0.127 mm Nominal Working Distance From 1 in./ 2.5 cm to 14 in. /35 cm on 100% UPC/EAN symbols Print Contrast 25% minimum reflective difference Roll (Tilt) 1 +/- 180 degrees from normal Pitch 2 +/- 60 degrees from normal Skew (Yaw) 3 +/- 50 degrees from normal

Decoding Capability

1D Codes UPC.EAN, UPC.EAN with Supplementals, UCC.EAN 128, JAN 8 & 13, Code 39, Code 39 Full ASCII, Code 39 Trioptic, Code 128, Code 128 Full ASCII, Codabar (NW7), Interleaved 2 of 5, Discrete 2 of 5,Code 93, MSI, Code 11, Code 32, Bookland EAN, IATA, UCC/EAN RSS and RSS variants 2D Codes PDF417, microPDF417, MaxiCode, DataMatrix (ECC 2000), Composite Codes, QR Code Postal Codes U.S. Postnet, U.S. Planet, U.K. Postal, Japan Postal, Australian Postal, Dutch Postal Interfaces Supported RS232, Keyboard Wedge, Wand Emulation, Scanner Emulation, IBM 468X/469X, USB and Synapse

User Environment

Operating Temperature 32° to 122° F/0° to 50° C Storage Temperature -40° to 158° F/-40° to 70° C Humidity 5% to 95% relative humidity, noncondensing Drop Specifications Multiple 6-foot (1.8 m) drops to concrete Ambient Light Immunity Immune to direct exposure of normal office and factory lighting conditions, as well as direct exposure to sunlight. Sunlight 10,000 ft. candles/107,644 LUX Electrostatic Discharge Conforms to 15 kV air discharge and 8 kV of contact discharge

Accessories

Hands-Free Intellistand 20-66483-01, Cash Register White; 20-66483-02, Twilight Black

Regulatory Information

Electrical Safety Certified to UL1950, CSA C22.2 No. 950, EN60950/IEC950 Laser Safety CDRH Class II, IEC Class 2 EMI/RFI FCC Part 15 Class B, ICES-003 Class B, European Union EMC Directive, Australian SMA

1 - Roll (Tilt): Controlled by rotating the wrist clockwise or counterclockwise 2 - Pitch: Controlled by dropping or raising the wrist 3 - Skew (Yaw): Controlled by rotating the wrist from left to right or vice versa

1 in./ 2.5 cm to 14 in. /35 cm